ESP32-C3-DevKit-Lipo
User Manual

Rev.1.0	September 2022
olimex.com

# What is ESP32-C3-DevKit-Lipo
ESP32-C3-DevKit-Lipo is Open Source Hardware Industrial grade -25+85ºC development board with:

- ESP32-C3 RISC-V single core processor runninig on 160 Mhz
- 384 KB ROM, 400 KB SRAM (16 KB for cache), 8 KB SRAM in RTC
- 4 MB embedded flash
- 2.4 GHz WiFi (802.11 b/g/n) 1T1R mode with data rate up to 150 Mbps
- Bluetooth® 5 module
- 15 GPIOs
- Onboard antenna
- Build in LiPo battery charger with STATUS LED, for handheld operations
- Lipo battery connector for Olimex LiPo batteries
- RESET button
- STATUS LED
- ICSP programming connector for rescue with ESP-PROG-C
- 4 mount holes
- USB-C connector for Debugging and Programming
- two soldered EXT headers with all signals and power supply

# ESP32-C3-DevKit-Lipo ordering options

ESP32-C3-DevKit-Lipo can be ordered as:
ESP32-C3-DevKit-Lipo

Additional accessories:
USB-C cable: CABLE-USB-A-C-1M
LiPo batteries: Olimex LiPo batteries
Breadboard: BREADBOARD1
Jumper wires: JW-200x10, JW-200x10-FM
# ESP32-C3-DevKit-Lipo Open Source Licensee
ESP32-C3-DevKit-Lipo is Open Source Hardware.

The Hardware files are released under CERN OSHW licensee.
The software is released under GPL 3 licensee.
The documentation is released under CC BY-SA 3.0 licensee.
# ESP32-C3-DevKit-Lipo software installation

Esspresif guide for Arduino IDE installation.
Esspressif guide for PlatformIO installation.
Espressif ESP-IDF installation.
JTAG debugging installation.

# ESP32-C3-DevKit-Lipo pinout description:

# ESP32-C3-DevKit-Lipo power supply and consumption

- 0.2A @ Active operation
- 22mA @ Idle
- 3mA @ Sleep
- 20 uA @ Power off
# ESP32-C3-DevKit-Lipo dimensions
# ESP32-C3-DevKit-Lipo schematic
# ESP32-C3-DevKit-Lipo schematic on GitHub
# Revision History
Revision 1.0 September 2022